## Slide 2: ADVANCED COMPUTER ARCHITECTURE
Dr. S. VAAHEEDHA KFATHEEN
ASSISTANT PROFESSOR
DEPARTMENT OF COMPUTER & IT
JAMAL MOHAMED COLLEGE (A)
TRICHY – 620 020.

## Slide 3: UNIT I – PARALLEL COMPUTER MODELS
1.1 STATE OF COMPUTING
Modern computers are equipped with powerful hardware facilities driven by extensive software packages.
To assess state-of-art computing, first review historical milestones in the development of computers.

## Slide 4: Cont.,
1.1.1 Computer Development Milestones
Computers have gone through two major stages of development:
    1. mechanical
    2. electronic
  Prior to 1945 computers were made with mechanical or electromechanical parts.
  The earliest mechanical computer can be traced back to 500 BC in the form of the abacus used in China.

## Slide 5
The abacus is manually operated to perform decimal arithmetic with carry propagation digit by digit.
Blaise Pascal built a mechanical adder/subtractor in France in 1642.
Charles Babbage designed a difference engine in England for polynomial evaluation in 1827.
Konrad Zuse built the first binary mechanical computer in Germany in 1941.
Cont.,

## Slide 6: Cont.,
Howard Aiken proposed the very first electromechanical decimal computer, which was built as the Harvard Mark I by IBM in 1944.
Both Zuse’s and Aiken’s machines were designed for general-purpose computations.
The fact that computing and communication were carried out with moving mechanical parts greatly limited the computing speed and reliability of mechanical computers.

## Slide 7: Cont.,
Modern computers were marked by the introduction of electronic components.
The moving parts in mechanical computers were replaced by high-mobility electrons in electronic computers.
Information transmission by mechanical gears or levers was replaced by electric signals traveling almost at the speed of light.

## Slide 8: Cont.,
COMPUTER GENERATION
Over the past five decades, electronic computers have gone through five generations of development.
Each of the first three generations lasted about 10 years.
The fourth generation covered a time span of 15 years.
Fifth generation use the processors and memory devices with more than 1 million transistors on a single silicon chip.

## Slide 9: Cont.,
The division of generations is marked primarily by sharp changes in hardware and software technologies.
The latest generation computers have inherited all the nice features and eliminated all the bad ones found in previous generations.

## Slide 10: Cont.,
PROGRESS IN HARDWARE
First Generation
As far as hardware technology is concerned, the first generation used vacuum tubes and relay memories interconnected by insulated wires.
Built with a single CPU which performed serial fixed-point arithmetic using a program counter, branch instructions, and an accumulator.
CPU must be involved in all memory access and input and output operations.
Machine and assembly languages were used.
Eg.,ENIAC

## Slide 11: Cont.,
Second Generation
The second generation was marked by the use of discrete transistors, diodes, and magnetic ferrite cores, interconnected by printed circuits.

## Slide 12: Cont.,
The third generation began to use integrated circuits for both logic and memory in small-scale or medium-scale integration and multilayered printed circuits.
The fourth generation used large-scale or very large-scale integration.
Semiconductor memory replaced core memory as computers moved from the third to the fourth generation.

## Slide 13: Cont.,
The fifth generation is highlighted by the use of high-density and high-speed processor and memory chips based even more improved VLSI technology.

## Slide 14: Cont.,
The first generation:-
From the architectural and software points of view, first generation computers were built with a single central processing unit which performed serial fixed-point arithmetic using a program counter, branch instructions, and an accumulator.
The CPU must be involved in all memory access and input/output operations.
Machine or assembly languages were used.
Eg., ENIAC – Electronic Numerical Integrator and Calculator

## Slide 15: Cont.,
The second generation
Index registers, floating-point arithmetic, multiplexed memory and I/O processors were introduced with second generation computers.
High level languages such as Fortran, Algol, and Cobol were introduced along with compilers, subroutine libraries and batch processing monitors.

## Slide 16: Cont.,
Register transfer language was developed for systematic design of digital computers.
Eg., IBM 7090, CDC 1604

## Slide 17: Cont.,
The third generation
The third generation was represented by the IBM/360 -370 series, the CDC 6600/7600 series, Texas instruments ASC(Advanced Scientific Computer)
Microprogrammed control became popular with this generation.
Pipelining and cache memory were introduced to close up the speed gag between the CPU and main memory.

## Slide 18: Cont.,
The idea of multiprogramming was implemented to interleave CPU and I/O activities across multiple user programs.
This led to the development of time-sharing operating systems using virtual memory with greater sharing or multiplexing of resources.

## Slide 19: Cont.,
The fourth generation
Parallel computers in various architectures appeared in the fourth generation of computers using shared or distributed memory or optional vector hardware.
Multiprocessing OS, special languages, and compilers were developed for parallelism.
Software tools and environments were created for parallel processing or distributed computing.
Eg., VAX 9000, IBM/ 3090

## Slide 20: Cont.,
The fifth generation
Fifth generation computers have just begun to appear.
These machines emphasize massively parallel processing (MPP)
Scalable and latency tolerant architectures are being adopted in MPP systems using VLSI silicon, high density packaging and optical technologies.

## Slide 21: Cont.,
- Fifth generation computers are targeted to achieve Teraflops performance by the mid 1990s
Heterogeneous processing is emerging to solve large scale problems using a network of heterogeneous computers with shared virtual memories.
Eg., Cray Research (MPP)

## Slide 22: Cont.,
1.1.2 Elements of Modern Computers
Hardware, software and programming elements of a modern computer system are briefly introduced below in the context of parallel processing.
Computing Problems
- A modern computers is an integrated system consisting of machine hardware, an instruction set, system software, application programs and user interfaces.

## Slide 23: Cont.,
The use of a computer is driven by real-life problems demanding fast and accurate solutions.
Depending on the nature of the problems, the solution may require different computing resources.
For numerical problems in science and technology, the solutions demand complex mathematical formulations and tedious integer or floating point computations.

## Slide 24: Cont.,
For alphanumeric problems in business and government, the solutions demand accurate transactions, large database management, and information retrieval operations.
For artificial intelligence problems and solutions demand logic inference and symbolic manipulations.
These computing problems have been labeled numerical computing, transaction processing and logical reasoning.

## Slide 25
Elements of a modern computer system
Hardware Architecture
O.S
Application Software
Performance
Evaluation
High-Level
Languages
Algorithms and Data Structures
Computing
Problems
Mapping
Programming
Binding
(Compile, Load)

## Slide 26: Cont.,
Algorithms and data structures
Special algorithms and data structures are needed to specify the computations and communications involved in computing problems.
Most numerical algorithms are deterministic, using regularly structured data.
Symbolic processing may use heuristic or nondeterministic searches over large knowledge base.

## Slide 27: Cont.,
Hardware Resources
A modern computer system demonstrates its power through coordinated efforts by hardware resources, an operating system and application software.
Processors, memory and peripheral devices form the hardware core of a computer system.
Special hardware interfaces are often built into I/O devices, such as terminals, workstations, optical page scanners, magnetic ink character recognizers, modems, file servers, voice data entry, printers, and plotter.
These peripherals are connected to mainframe computers directly or through local or wide area networks.

## Slide 28: Cont.,
In addition, software interface programs are needed.
These software interfaces include file transfer systems, editors, word processors, device drivers, interrupt handlers, network communication programs etc.,

## Slide 29: Cont.,
Operating System
As effective operating system manages the allocation and deallocation of resources during the execution of user programs.
Mapping is a bidirectional process matching algorithmic structure with hardware architecture and vice versa.
Efficient mapping will benefit the programmer and produce better source codes.
The mapping of algorithmic and data structures onto the machine architecture includes processor scheduling, memory maps, interprocessor communications, etc.,
These activities are usually architecture-dependent.

## Slide 30: Cont.,
Parallelism can be exploited at algorithm design time, at program time, at compile time and at run time.
Techniques for exploiting parallelism at these levels form the core of parallel processing technology.

## Slide 31: Cont.,
System Software Support
Software support is needed for the development of efficient programs in high-level languages.
the source code written in a HLL must be first translated into object code by an optimizing complier.
The compiler assigns variables to registers or to memory words and reserves functional units for operators.
An assembler is used to translate the compiled object code into machine code which can be recognized by the machine hardware.
A loader is used to initiate the program execution through the OS kernel.

## Slide 32: Cont.,
Compiler support
- There are three compiler upgrade approaches: preprocessor, precompiler and parallelizing compiler.
A preprecessor uses a sequential compiler and a low-level library of the target computer to implement high level parallel constructs.
The precompiler approach requires some program flow analysis, dependence checking and limited optimizations toward parallelism detection.

## Slide 33: Cont.,
The third approach demands a fully developed parallelizing or vectorizing compiler which can automatically detect parallelism in source code and transform sequential codes into parallel constructs.
The efficiency of the binding process depends on the effectiveness of the preprocessor, the precompiler, the prallelizing complier, the loader, and the OS support.

## Slide 34: 1.1.3 Evolution of Computer Architecture
The study of computer architecture involves both hardware organization and programming/software requirements.
As seen by an assembly language programmer, computer architecture is abstracted by its instruction set, which includes opcode, addressing modes, registers, virtual memory etc.,

## Slide 35: Cont.,
From the hardware implementation point of view, the abstract machine is organized with CPUs, caches, buses, microcode, pipelines, physical memory, etc.,

## Slide 36: Cont.,
Lookahead, Parallelism and Pipelining
Lookahead techniques were introduced to prefetch instructions in order to overlap.
I/E operations and to enable functional parallelism.
Functional parallelism was supported by two approaches:
  One is to use multiple functional units simultaneously
  The other is to practice pipelining at various processing levels.

## Slide 37: Cont.,
Flynn’s Classification
Michael Flynn (1972) introduced a classification of various computer architecture based on notions of instructions and data streams.
Conventional sequential machines are called SISD ( Single Instruction stream over a single data stream) computers.

## Slide 38: Cont.,
Vector computers are equipped with scalar and vector hardware or appear as SIMD ( single instruction stream over multiple data streams) machines.
Parallel computers are reserved for MIMD (multiple instruction streams over multiple data streams) machines.
An MISD ( multiple instruction streams and a single data stream) machines.
The same data stream flows through a linear array of processors executing different instruction streams.
This architecture is also known as systolic arrays fro pipelined execution of specific algorithms.

## Slide 39: Cont.,
Of the four machine models, most parallel computers build in the past assumed the MIMD model for general purpose computations.
The SIMD and MISD models are more suitable for special purpose computations.
For this reason, MIMD is the most popular model, SIMD next, and the least popular model being applied in commercial machines.

## Slide 40: Cont.,
Parallel/ Vector Computers
Intrinsic parallel computers are those that execute programs in MIMD mode.
There are two major classes of parallel computers, namely, shared memory multiprocessors and message passing multicomputers.
The major distinction between multiprocessors and multicomputers lies in memory sharing and the mechanisms used for interprocessor communication.

## Slide 41: Cont.,
The processors in a multiprocessor system communicate with each other through shared variables in a common memory.
Each computer node in a multicomputer system has a local memory, unshared with other nodes.
Interprocessor communication is done through message passing among the nodes.

## Slide 42: Cont.,
Explicit vector instructions were introduced with the appearance of vector processors.
A vector processor is equipped with multiple vector pipelines that can be concurrently used under hardware or firmware control.
There are two families of pipelines vector processors
Memory-to-memory architecture supports the pipelined flow of vector operands directly from the memory to pipelines and then back to the memory.

## Slide 43: Cont.,
Register-to-register architecture uses vector registers to interface between the memory and functional pipelines.
Another important branch of the architecture tree consists of the SIMD computers for synchronized vector processing.
SIMD computing is achieved through the use of an array of processing elements synchronized by the same controller.
Associative memory can be used to build SIMD associative processors.

## Slide 44: SISD uniprocessor architecture
Where,
  IS – Instruction Stream
  DS – Data Stream
Control Unit
Processing Unit
Memory Unit
Instruction Stream
I/O
DS
IS

## Slide 45: SIMD architecture ( with distributed memory)
CU
PE1
PEn
LMn
LM1
IS
IS
DS
DS
DS
DS
Data sets loaded from host
Program loaded from host
.
.
.
.
.
.
.
.
.
.

## Slide 46: MIMD architecture (with shared memory)
CU1
CUn
PUn
PU1
Shared Memory
IS
IS
DS
DS
IS
IS
I/O
I/O
.
.
.
.
.
.
.
.
.
.
.
.

## Slide 47: MISD architecture (the systolic array)
Memory
( program and data)
CU1
IS
PUn
CUn
CU2
PU1
PU2
IS
IS
IS
IS
DS
DS
DS
DS
i/O

## Slide 48: Flynn’s classification of computer architectures
Applications
Programming Environment
Language Supported
Communication Model
Addressing Space
Hardware Architecture
Machine Independent
Machine Dependent

## Slide 49: Cont.,
Development layers
Hardware configurations differ from machine to machine, even those of the same model.
The address space of a processor in a computer system varies among different architectures.
It depends on the memory organization, which is machine-dependent.

## Slide 50: Cont.,
To develop application programs and programming environments which are machine independent.
Independent of machine architecture, the user programs can be ported to many computers with minimum conversion costs.
HLL and communication models depend on the architectural choices made in a computer system.

## Slide 51: Cont.,
New Challenges
- The technology of parallel programming is the outgrowth of four decades of research and industrial advances in microelectronics, printed circuits, high density packaging, advanced processors, memory systems, peripheral devices, communication channels, language evolution, compiler sophistication, operating systems, programming environments, and application challenges.

## Slide 52: Cont.,
- Representative real-life problems include weather forecast, modeling, computer-aided design of VLSI circuits, large-scale database management, artificial intelligence, crime control, and strategic defense initiatives, just to name a few.
- The application domains of parallel processing computers are expanding steadily.

## Slide 53: Cont.,
Clock Rate and CPI
The CPU of today’s digital computer is driven by a clock with a constant cycle time.
The inverse of the cycle time is the clock rate.
The size of a program is determined by its instruction count in terms of the number of machine instructions to be executed in the program.
Different machine instructions may require different numbers of clock cycles to execute.
The cycles per instruction becomes in important parameter for measuring the time needed to execute each instruction.

## Slide 54: Cont.,
For a given instruction set, calculate an average CPI over all instruction types.
An accurate estimate of the average CPI requires a large amount of program code to be traced over a long period of time.

## Slide 55: Cont.,
Performance Factors
Let Ic be the number of instructions in a given program, or the instruction count.
The CPU time needed to execute the program is estimated by finding the product of three contributing factors:
T = Ic * CPI *

## Slide 56: Cont.,
- The execution of an instruction requires going through a cycle of events involving the instruction fetch, decode, operand fetch, execution, and store results.
In this cycle, only the instruction decode and execution phases are carried out in the CPU.
The remaining three operations may be required to access the memory.
A memory cycle as the time needed to complete one memory reference.

## Slide 57: Cont.,
The CPI of an instruction type can be divided into two component terms corresponding to the total processor cycles and memory cycles needed to complete the execution of the instruction.
Depending on the instruction type, the complete instruction cycle may involve one to four memory references.
  T = Ic * (p + m* k) *

## Slide 58: Cont.,
System Attributes
The above five performance factors are influenced by four system attributes:
  1. instruction-set architecture
  2. compiler technology
  3. CPU implementation and control
  4. cache and memory hierarchy

## Slide 59: Cont.,
The instruction set architecture affects the program length and processor cycle needed.
The compiler technology affects the values of Ic,p and the memory reference count (m)
The CPU implementation and control determine the total processor time needed.
- Finally, the memory technology and hierarchy design affect the memory access latency.

## Slide 60: Cont.,
MIPS Rate
The processor speed is often measured in terms of million instructions per second.
MIPS rate varies with respect to a number of factors, including the clock rate, the instruction count and the CPI of a given machine.

## Slide 61: Cont.,
Throughput Rate
Another important concept if related to how many programs a system can execute per unit time, called the system throughput.
In a multiprogrammed system, the system throughput is often lower than the CPU throughput Wv defined by
Wv = f / Ic * CPI

## Slide 62: Cont.,
Programming Environments
The programmability of a computer depends on the programming environment provided to the users.
Most computer environments are not user-friendly.
Conventional uniprocessor computers are programmed in a sequential environment in which instructions are executed one after another in a sequential manner.

## Slide 63: Cont.,
Most existing compilers are designed to generate sequential object codes to urn on a sequential computer.
In other words, conventional computers are being used in a sequential programming environment using languages, compilers and operating systems all developed for a uniprocessor computer.

## Slide 64: Cont.,
When using a parallel computer, one desires a parallel environment where parallelism is automatically exploited.
Language extensions or new constructs must developed to specify parallelism or to facilities easy detection of parallelism at various granularity levels by more intelligent compilers.

## Slide 65: Cont.,
Besides parallel languages and compilers, the operating system must be also extended to support parallel activities.
The OS must be able to manage the resources behind parallelism.
Important issues include parallel scheduling of concurrent events, shared memory allocation and shared peripheral and communication links.

## Slide 66: Implicit parallelism
Implicit parallelism
An implicit approach uses a conventional language, such as C, Fortran, Lisp or Pascal to write the source program.
The sequentially coded source program is translated into parallel object code by a parallelizing compiler.

## Slide 67: Implicit parallelism
PErogrammerEPP:
S
Source code written in sequential languages C, Fortran, Lisp, or Pascal
Parallelizing compiler
Parallel Object code
Programmer
Execution by runtime system

## Slide 68: Explicit parallelism
The second approach requires more effort by the programmer to develop a source program using parallel dialects of C, Fortran, Lisp or Pascal
Parallelism is explicitly specified in the user programs.
This will significantly reduce the burden on the compiler to detect parallelism.

## Slide 69: Explicit parallelism
PErogrammerEPP:
S
Source code written in concurrent dialects C, Fortran, Lisp, or Pascal
Concurrency preserving compiler
Concurrent Object code
Programmer
Execution by runtime system

## Slide 70: MULTIPROCESSORS AND MULTICOMPUTERS
Introduction
Two categories of parallel computers are architecturally modeled.
1. Shared common memory
2. Unshared distributed memory

## Slide 71: Cont.,
Shared-Memory Multiprocessors
Three shared memory multiprocessor models
1. uniform memory access
2. nonuniform memory access
3. cache-only memory architecture

## Slide 72: Cont.,
UMA
Physical memory is uniformly shared by all the processors
All processors have equal access time to all memory words
Each processor may use a private cache
Peripherals are also shared or distributed.
Multiprocessors are tightly coupled systems due to the high degree of resource sharing.

## Slide 73: Cont.,
The system takes the form of a common bus, a crossbar switch or a multistage network.
Suitable for general purpose and time sharing applications by multiple users
It can be used to speed up the execution of a single large program in time critical applications.
To coordinate parallel events, synchronization and communication among processors are done through using shared variables in the common memory.

## Slide 74: Cont.,
When all processors have equal access to all peripheral devices, the system is called a symmetric multiprocessor.
In this case, all the processors are equally capable of running the executive programs, such as the OS kernel and I/O service routines.
In an asymmetric multiprocessor, only one or a subset of processors are executive capable.
An executive or a master processor can execute the OS and handle I/O

## Slide 75: Cont.,
The remaining processors have no I/O capability and thus are called attached processors.
Attached processors execute user codes under the supervision of the master processor.

## Slide 76
NUMA
A NUMA multiprocessor is a shared-memory system in which the access time varies the location of the memory word.
The shared memory is physically distributed to all processors, called local memories.
The collection of all local memories forms a global address space accessible by all processors.

## Slide 77: Cont.,
It is faster to access a local memory with a local processor.
The access of remote memory attached to other processors takes longer due to the added delay through the interconnection network.
Besides distributed memories, globally shared memory can be added to a multiprocessor system.

## Slide 78: Cont.,
In this case, there are three memory-access patterns:
  1. fastest memory is local memory access
  2. global memory access
  The slowest is access of remote memory.
  The processors are divided into several clusters.
  Each cluster is itself an UMA or a NUMA multiprocessor.
  The clusters are connected to global shared-memory modules.

## Slide 79: Cont.,
The entire system is considered a NUMA multirpocessor.
All processors belonging to the same cluster are allowed to uniformly access the cluster shared-memory modules.
All clusters have equal access to the global memory.

## Slide 80: Cont.,
COMA
A multiprocessor using cache-only memory assumes the COMA model.
The COMA model is a special case of a NUMA machine, in which distributed main memories are converted to caches.
There is no memory hierarchy at each processor node.
All the caches form a global address space.
Remote cache access is assisted by the distributed cache directories.

## Slide 81: Cont.,
- Depending on the interconnection network use, sometimes hierarchical directories may be used to help locate copies of cache blocks.
Initial data placement is not critical because data will eventually migrate to where it will be used.
Besides the UMA,NUMA, and COMA models specified above, other variations exist for multiprocessors.
For example, a cache-coherent non-uniform memory access model can be specified with distributed shared memory and cache directories.

## Slide 82: Cont.,
Distributed-Memory multicomputers
- A distributed-memory multicomputer system consists of multiple computers, often called nodes, interconnected by a message- passing network.
- Each node is an autonomous computer consisting of a processor, local memory, and sometimes attached disks or I/O peripherals.

## Slide 83: Cont.,
The message-passing network provides point-to-point static connections among the nodes.
All local memories are private and are accessible only by local processors.
For this reason, traditional multicomputers have been called no-remote-memory-access machines.

## Slide 84: Cont.,
Multicomputer Generations
Modern multicomputers use hardware routers to pass messages.
A computer node is attached to each router.
The boundary router may be connected to I/O and peripheral devices.
Message passing between any two nodes involves a sequence of routers and channels.
Mixed types of nodes are allowed in a heterogeneous multicomputer.

## Slide 85: Cont.,
The internode communications in a heterogeneous multicomputer are achieved through compatible data representations and message passing protocols.
Message-passing multicomputers have gone through two generations of development, and a new generation is emerging.
First generation
  Based on processor technology
  Hypercube architecture
  Software controlled message switching

## Slide 86: Cont.,
Second generation
  Mesh-connected architecture
  Hardware message routing
  Third generations
  - fine-grain multicomputers
  Important issues for multicomputers include message-routing schemes, network flow control strategies, deadlock avoidance, virtual channels.

## Slide 87: Cont.,
A Taxonomy of MIMD computers
Parallel computers appear as either SIMD or MIMD configurations
SIMDs appeal more to special purpose applications.
SIMDs are not size-scalable, but unclear whether large SIMDs are generation-scalable.
Multicomputers use distributed memories with multiple address space.

## Slide 88: Multivector and SIMD Computers
Vector Supercomputers
A vector computer is often built on top of a scalar processor.
Vector processor is attached to the scalar processor as an optional feature
Program and data are first loaded into the main memory through a host computer.
All instructions are first decoded by the scalar control unit.
If the decoded instruction is a scalar operation or a program control operation, it will be directly executed by the scalar processor using the scalar functional pipelines.

## Slide 89: Cont.,
If the instruction is decoded as a vector operation, it will be sent to the vector control unit.
This control unit will supervise the flow of vector data between the main memory and vector functional pipelines.
The vector data flow is coordinated by the control unit.

## Slide 90: Vector processor models
Two pipeline vector supercomputer models
      Register-to-register
      Memory-to-memory
    Register-to-register
    Vector registers are used to hold the vector operands, intermediate and final vector results.
    The vector functional pipelines retrieve operands from and put results into the vector registers.
    All vector registers are programmable in user instructions
    Each vector registers used in successive pipeline cycles.

## Slide 91: Cont.,
The length of each vector register is usually fixed.
There are fixed numbers of vector registers and functional pipelines in a vector processor.
Both resources must be reserved in advance to avoid resource conflicts between different vector operations.

## Slide 92: Cont.,
Memory-to-memory
Differs from a register-to-register architecture
In the use of a vector stream unit to replace the vector registers.
Over a dozen pipelined vector computers have been manufactured, ranging from workstations to mini- and supercomputers.

## Slide 93: Cont.,
SIMD Supercomputers
An operational model of an SIMD computer is specified by a 5-tuple
M = ( N, C, I, M, R)
Where,
N is the number of processing elements in the machine.
C is the set of instructions directly executed by the control unit

## Slide 94: Cont.,
I is the set of instruction broadcast by the control unit to all PEs for parallel execution.
M is the set of masking schemes.
R is the set of data-routing functions, specifying various patterns.

## Slide 95: REFERECES
Kai Hwang, “Advanced Computer
Architecture, “McGraw-Hill International
Edition Singapore, 1993