## Slide 1: C0MPUTER ARCHITECTURE
Dr.S.Vaaheedha Kfatheen
Assistant Professor
Department of Computer Science & IT
Jamal Mohamed College (A)
Trihy – 620 020.

## Slide 2: Advanced Processor Technology
VLSI microprocessors used in workstations or multiprocessors to heavy-duty processors used in mainframes and supercomputers.
Major processor families are
    CISC
    RISC
    Superscalar’
    VLIW
    Superpipelined
    Vector
    Symbolic processors

## Slide 3: Cont.,
Scalar and vector processors are for numerical computations
Symbolic processors are developed for AI applications.

## Slide 4: Design space of processors
Various processor families can be mapped onto a coordinated space of clock rate versus cycles per instruction.
As implementation technology evolves rapidly, the clock rates of various processors are gradually moving from low to higher speeds toward the right of the design space.
Processor manufactures are trying to lower the CPI rate using hardware and software approaches.

## Slide 5: The Design Space
Conventional processors like Intel i486, fall into the family known as complex-instruction-set computing (CISC) architecture.
Clock rate ranges from 33 to 50 MHz
With microprogrammed control, CPI of different CISC instructions varies from 1 to 20.
Reduced-instruction-set computing (RISC) processors, Intel i860 have faster clock rates ranging from 20 to 120 MHz.
Use of hardwired control, the CPI of most RISC instructions has been reduced to one to two cycles.

## Slide 6: Cont.,
A special subclass of RISC processors are the superscalar processors, which allow multiple instructions to be issued simultaneously during each cycle.
The CPI should be lower than that of a generic scalar RISC processor.
The clock rate of superscalar processors matches that of scalar RISC processors.
The Very Long Instruction Word uses even more functional units than that of a superscalar processor.
CPI of a VLIW can be further lowered.
VLIW have been implemented with microprogrammed control.
Clock rate is slow with the use of read-only memory.
A large number of microcode access cycles may be needed for some instructions.

## Slide 7: Cont.,
Superpipelined processors are multiphase clocks with a much increased clock rate ranging from 100 to 500 MHz.
The processors in vector supercomputers are mostly superpipelined and functional units for concurrent scalar and vector operations.

## Slide 8: Instruction Pipelines
The execution cycle of a typical instruction includes four phases:
  Fetch
  Decode
  Execute
  Write-back
These instruction phases are often executed by an instruction pipeline.
The pipeline, like an industrial assembly line, receives successive instructions from its input end and executes them in a streamlined, overlapped fashion as they flow through.
A pipeline cycle is defined as the time required for each phase to complete its operation, assuming equal delay in all phases.

## Slide 9: Cont.,
Instruction pipeline cycle
  The clock period of the instruction pipeline
Instruction issue latency
  The time required between the issuing of two adjacent instructions
Instruction issue rate
  The number of instructions issued per cycle
Simple operation latency
  Simple operations make up the vast majority of instructions executed by the machine, such as integer adds, loads, stores, branches, moves, etc.
  Complex operations are those requiring an order-of-magnitude longer latency, such as divides, cache misses etc.,
Resource conflicts
  Two or more instructions demand use of the same functional unit at the same time

## Slide 10: References
1.Kai Hwang and Faye A.Briggs, “Computer Architecture and Parallel
Processing”, McGraw-Hill International Edition, Singapore, 1985. 2.Michael J.Quinn, “Parallel Computing, Theory and Practice”,
McGrawHill, International Edition, Singapore1994.