## Slide 2: BINARY CODES
Dr.S.Vaaheedha Kfatheen
Assistant Professor
Department of Computer Science & IT
Jamal Mohamed College (A)
Trichy- 620 020.

## Slide 3: INTRODUCTION
Even though the binary number system has many practical advantages and is widely used in digital computers.
In many cases it is convenient to work with decimal number system.
For better interaction between man and computer, it will be good if the computers read input data in decimal form and print or display output in decimal form.

## Slide 4
To facilitate this interaction, many binary codes have been developed.
By means of these codes, decimal digits are represented by sequences of binary digits.
A simple form of one such code is binary coded decimal codes, or simply BCD codes.

## Slide 5: 1. BCD CODES
A group of bits which are used to represent decimal numbers 0 to 9 are called to Binary Coded Decimal codes or BCD codes.
The 8421 indicates the binary weights of 4-bits (23, 22,21,20) for numbers 0-9 .
Any number greater than 9 can be represented in 8421 BCD, by repeatedly using the 4-bit code for each digit.

## Slide 6
S.NO | DECIMAL NUMBER | BCD
1 | 0 | 0000
2 | 1 | 0001
3 | 2 | 0010
4 | 3 | 0011
5 | 4 | 0100
6 | 5 | 0101
7 | 6 | 0110
8 | 7 | 0111
9 | 8 | 1000
10 | 9 | 1001
 | For numbers > 9 | 
11 | 26 | 0010 0110
12 | 13 | 0001 0011
13 | 74 | 0111 0100
14 | 56 | 0101 0110

## Slide 7: 2. SELF COMPLEMENTING CODES
If a binary code representing a decimal digit D is constructed such that when we complement each bit, we obtain the code for (9-D), it is called a self complementing code.
That is in a self complementing code the 1s complement of the BCD must be equal to the BCD of the 9s complement of the decimal.

## Slide 8
For example 84-2-1, 2421 and 4221 codes are self complementing weighted codes.
A necessary condition for a weighted code to have self complementing property is that the sum of the weights used must be equal to 9
(8+4-2-1 = 9 and 2+4+2+1=9).
But a self complementing code need not necessarily be a weighted code.
An important, unweighted self complementing code is the Excess-3 code.

## Slide 9
DECIMAL | 2421 | 4221
0 | 0000 | 0000
1 | 0001 | 0001
2 | 0010 | 0010
3 | 0011 | 0011
4 | 0100 | 0110
5 | 1011 | 1001
6 | 1100 | 1100
7 | 1101 | 1101
8 | 1110 | 1110
9 | 1111 | 1111

## Slide 10
2421 CODE: Example
  Binary code for 4 = 0100
  9’s complement of 4 = 1011 = 5
  The 1’s complement of 4 is 5 which is 1’s complement of 4.
  4221 CODE: Example
  Binary code for 4 = 0110
  1’s complement of 4 = 1001 = 5
  The 1’s complement of 4 is 5 which is the 9’s complement of 4.
  The 2421 and 4221 codes are also called as weighted codes

## Slide 11
R’s2’s
R-1’s
Binary code of a decimal number is complemented, the binary code representing the 9’s complement of the decimal number.
4- decimal = 0100 (2421)
1’s complement – 1011
Decimal - 5

## Slide 12
6-i/p 0110
Decimal – 2421 binary
Binary – 1’s (0110=1001)
1’s – decimal – 3 – o/p
9-6=3

## Slide 13
0110
1001 – 1’s
5
9-5=4 – 9’s

## Slide 14: EXCESS – 3 CODE
The Excess-s code is another BCD code.
The Excess-s code for a decimal digit is obtained by adding 0011(3) to the 8421 code.
It has 10 valid codes and 6 invalid codes.
The 6 invalid codes are
0000 1101
0001 1110
0010 1111

## Slide 15
8 4 2 1 (5)
  0 1 0 1 - 8421 (binary code)
  1 1 +
  1 0 0 0 - Excess-3(binary code)

## Slide 16
In Excess-3 if any number is greater than 9 then the code is given separately for each digit.
Excess-3 is not a weighted code.
Excess-3 is a self-complementing code

## Slide 17
S.NO | DECIMAL NUMBER | 8421 | Excess-3
1 | 0 | 0000+0011 | 0011
2 | 1 | 0001 | 0100
3 | 2 | 0010 | 0101
4 | 3 | 0011 | 0110
5 | 4 | 0100 | 0111
6 | 5 | 0101+0011 | 1000
7 | 6 | 0110 | 1001
8 | 7 | 0111 | 1010
9 | 8 | 1000 | 1011
10 | 9 | 1001 | 1100
 | For numbers > 9 |  | 
10 | 26 | 0010 0110+0011 | 0101 1001
11 | 97 | 1001 0101 | 1100 1010
12 | 853 | 1000 0101 0011 | 1011 1000 0110

## Slide 18: GRAY CODES
Gray code is an unweighted code in which successive numbers differ in only one bit position.
Such codes are used in analog to digital conversion.
The Gray code is a standard binary code, and not a weighted code.
The Gray code of a decimal number can be obtained by converting binary number using specific procedures.

## Slide 19
Gray code is not convenient for arithmetic operation.
Such a code in which not more than one bit differs from its neighbours is called Gray code or cyclic code or reflected code.
This concept is formalized by defining what is known as hamming distance.
The hamming distance between two binary codes of equal length is the number of bit positions in which they differ.

## Slide 20
For example, if A=0110 and B=1010 the hamming distance between A and B is two, since they differ in two bit position.
Hamming distance between two successive code groups in a cyclic code is unity.

## Slide 21
Rules for converting binary to gray
1. The MSB of the gray code is the same as the MSB of the binary
2. Coding from left to right, add each adjacent pair of bits to get the next bit of the gray code.
Omit the carries, if occurs.

## Slide 22
The following formulae define binary to gray conversion
Let B = BnBn-1Bn-2……B0 represent a natural binary number
Let G = GnGn-1Gn-2…….G0 represent equivalent gray code
Then
Gn = Bn
Gn-1 = Bn + Bn-1

## Slide 23
Eg.,
Convert the binary number 1011 to gray code.
Step1: 1 0 1 1 Step3: 1 0 + 1 1
1 1 1 1
Step2: 1 + 0 1 1 Step4: 1 0 1 + 1
1 1 1 1 1 0
(1011)2 = (1110)G

## Slide 24
Example:
Binary 1101 1110 1001 0111
Gray 1011 1001 1101 0100

## Slide 25
Rules for converting Gray to Binary
1. The MSB of the binary is the same as the MSB of the Gray
2. Coding from left to right add the binary digit generated to the adjacent gray bit to get the next bit of the binary
3. Omit the carries, if occurs.

## Slide 26
The following formulae define binary to gray conversion
Let G = GnGn-1Gn-2…….G0 represent a Gray code
Let B = BnBn-1Bn-2……B0 represent a equivalent Binary code
Then
Bn = Gn
Bn-1 = Bn + Gn-1

## Slide 27
Convert the Gray code 1110 to Binary
Step1: 1 1 1 0 Step3: 1 1 1 0
1 +
Step2: 1 1 1 0 1 0 1
+ Step4: 1 1 1 0
1 0 +
1 0 1 1

## Slide 28
Example
Gray 0111 0100 1101 1110
Binary 0101 0111 1001 1011

## Slide 29: ALPHANUMERIC CODES
1. ASCII Code
ASCII is an alphanumeric code which stands for American Standard Code for Information Interchange.
ASCII is a 7-bit code that is used to represent decimal digits 0 to 9, alphabets A to Z both cases and some special characters
In ASCII, there are 27 = 128 possible binary combinations

## Slide 30
ASCII also includes some control characters like DEL, ESC, STX(START of Text), ETX (End of Text) etc.

## Slide 31
ASCII Symbol | Decimal | Hexa | 7-Binary
0 | 48 | 30 | 011 0000
1 | 49 | 31 | 011 0001
2 | 50 | 32 | 011 0010
9 | 57 | 39 | 011 1001
. . |  |  | 
. . |  |  | 
A | 65 | 41 | 100 0001
B | 66 | 42 | 100 0010
a | 97 | 61 | 110 0001
b | 98 | 62 | 110 0010
DEL | 127 | 7F | 111 1111

## Slide 32
2. EBCDIC
EBCDIC stands for Extended Binary Coded Decimal Interchange Code.
Another alphanumeric codes used in IBM machine is the EBCDIC
It uses 8-bit for each character and a ninth bit for parity.
It has the same character symbols as ASCII but the bit assignment to character is different.

## Slide 33: References
1. Albert Paul Malvino, Donald P. Leach and
Goutam Saha, Digital Principles and
Applications, TMH, Sixth Edition, 2007. 2.Morris Mano M, Computer System
Architecture, PHI, Third Edition, 2008